ECE 256 Midterm Exam                      18 April 2009

Spring Semester

Name:

Number:					                                    Signature:

| 1 | 2 | 3 | total |
| --- | --- | --- | --- |
| 20 | 40 | 40 | 100 |

Open book and open notes.

Good luck (

Answers without necessary steps will not get any credit.

1) Evaluate           over the surface of a sphere of a radius R=1.  This sphere is centered at the origin.(20)

2)   exist in the region of cylindrical shell formed by two cylinders defined by ri = 1 and ro = 2, and height is h = 5.  Evaluate

- (20)

- (20)

ro                         ri

h=5

3) A spherical capacitor consists of an inner conducting sphere of radius Ri and an outer spherical conducting shell of inner radius Ro.  The space between Ri < R ≤ R1 is filled with a dielectric permittivity of ε1 and the space between R1 < R ≤  R2 is filled with a dielectric permittivity of ε2.  There is air between R2 < R ≤  Ro.

a) Determine the capacitance of the system (30)

b) Discuss the case for Ro ( . (10)

Ro

air

ε2

ε1

Ri

R1

R2