ECE 256 Midterm Exam              4 May 2009

Spring Semester

SOLUTIONS

| 1 | 2 | 3 | total |
| --- | --- | --- | --- |
| 20 | 40 | 40 | 100 |

Open book and open notes.

Good luck (

Answers without necessary steps will not get any cre

1) Evaluate           over the surface of a sphere of a radius R=1.  This sphere is centered at the origin.(20)

/

1 2)   exist in the region of cylindrical shell formed by two cylinders defined by ri = 1 and ro = 2, and height is h = 5.  Evaluate

= 

E2 and E3 are similar

3) A spherical capacitor consists of an inner conducting sphere of radius Rj and an outer spherical conducting shell of inner radius Ro. The space between Rj < R:s R1 is filled with a dielectric pennittivity of £1 and the space between R1 < R:s R2 is filled with a dielectric permittivity of £2. There is air between R2 < R:s Ro.

- Determine the capacitance of the system (30)

- Discuss the case for Ro -7 co. (10)